## Slide 1: Virtualization of a Real-Time Operating System for Robot Control with a Focus on Real-Time Compliance
Halil Pamuk, BSc.
Sebastian Rauh, MSc. Beng.

## Slide 2: Introduction
Robots perform time-critical tasks
Real-time = deterministic and predictable
Delays  catastrophic consequences
General-Purpose Operating System vs. Real-Time Operating System
Figure 1: Non-preemptible Kernel [1]
Figure 2: Preemptible Kernel [1]
Process A
User
space
Process A
Process B
Process A
preempted
Kernel
space
Process A
User
space
Process A
Process B
Process B
Interrupt handler
Scheduler
System call handler
Device Interrupt
Timer Interrupt
System call
Kernel
space
Process A
resumes
Time
Time

## Slide 3: Problem and Task Definition
Research Question: Is it possible, and if so, how can the latency of a real-time operating system virtualization be reduced using Yocto, Xenomai, and QEMU to a level that is closer to that of bare metal (below 50 μs)?
Virtualization of Real-Time Operating Systems | 
Advantages | Disadvantages
Scalability & flexibility | Increased overhead and latency
Cheaper | Performance variability
Remote management | Complexity

## Slide 4: Application Context and Conditions
This work was written at SIGMATEK GmbH & Co KG
Host OS: Ubuntu 22.04.4 LTS, PREEMPT-RT
Guest OS: Salamander 4
  Built with Yocto [2]
  Virtualized through Quick Emulator (QEMU) [3]
  Hard real-time with Xenomai 3 [4]
Trace-cmd [5] and Kernelshark [6] for kernel tracing and visualization

## Slide 5: Methodology
Initial Situation
Measure initial latency difference between bare metal & untuned virtualization
with the latency tool of Xenomai
Real-Time Performance Tunings
Sequentially tune virtualization through configurations of
BIOS, kernel, host, guest and QEMU
Latency Comparison
Compare the latency after the tunings with the latency tool
Robotic Application
Validate the tunings with a real-time robotic application

## Slide 6: Results – Latency Comparison
10 minutes with a sampling period of 100 µs, priority of 99
Table 1: Comparison of Latency Results
Figure 1: Comparison of Latency Distributions
Samples
Time in μs
1
10
100
200
400
800

## Slide 7: Results – Robotic Application
Difference between command issuance time and signal arrival at PWM
1,000 samples
Table 2: Comparison of Robotic Application Latency Results

## Slide 8: Discussion
Latency Tool
Worst latency decreased from 707.622 µs to 17.134 µs
Close to bare metal’s 10.709 µs
No overruns
Goal achieved
Robotic Application
Worst latency dropped from 129 ms to 3.988 ms
Close to bare metal’s 1.49 ms
Tunings validated

## Slide 9: Outlook
Additional configurations
Other hypervisors and virtualization technologies
More testing under workloads

## Slide 10: References
[1] https://ubuntu.com/blog/what-is-real-time-linux-ii
[2] https://docs.yoctoproject.org/
[3] https://www.qemu.org/
[4] https://xenomai.org/
[5] https://trace-cmd.org/
[6] https://kernelshark.org/

## Slide 11: Salamander 4 Bare Metal

## Slide 12: Salamander 4 Untuned Virtualization

## Slide 13: Salamander 4 Bare Metal vs. Virtualization

## Slide 14: Salamander 4 Virtualization BIOS Configurations

## Slide 15: Salamander 4 Virtualization after BIOS Configurations

## Slide 16: Salamander 4 Virtualization Kernel Configurations

## Slide 17: Salamander 4 Virtualization after Kernel Configurations

## Slide 18: Salamander 4 Virtualization Host Configurations

## Slide 19: Salamander 4 Virtualization after Host Configurations

## Slide 20: Salamander 4 Virtualization QEMU Configurations

## Slide 21: Priorities for Different Scheduling Policies

## Slide 22: Salamander 4 Virtualization after QEMU Configurations

## Slide 23: Robot

## Slide 24: Servo Motor with PWM module

## Slide 25: Servo Motor Function

## Slide 26: Robotic Application Setups

## Slide 27: Robotic Application Flowchart

## Slide 28: Results of Robotic Application

## Slide 29: Host Operating System

## Slide 30: Xenomai Approaches

## Slide 31: QEMU Script

## Slide 32: Trace-cmd

## Slide 33: Trace-cmd
sudo trace-cmd record -e all -A @3:823 -name Salamander4 -e all
sudo trace-cmd record -e kvm:kvm_entry -e kvm:kvm_exit -A @3:823 -name Salamander4 -e all
sudo trace-cmd record -e kvm -e sched -e irq -e -A @3:823 -name Salamander4 -e all

## Slide 34: Kernelshark