## Slide 1: Virtualization of a Real-Time Operating System for Robot Control with a Focus on Real-Time Compliance
Halil Pamuk, BSc.
Sebastian Rauh, MSc. Beng.

## Slide 2: Introduction
Robots perform time-critical tasks
Delays  catastrophic consequences
General-Purpose Operating System vs. Real-Time Operating System
Figure 1: Non-preemptible Kernel [1]
Figure 2: Preemptible Kernel [1]

## Slide 3: Problem and Task Definition
Task: Bring latency of virtualization closer to bare metal (below 50 μs)
Virtualization of Real-Time Operating Systems | 
Advantages | Disadvantages
Scalability & flexibility | Increased overhead and latency
Cheaper | Performance variability
Remote management | Complexity

## Slide 4: Methodology
Asses Initial Situation
Measure initial latency difference between bare metal & untuned virtualization with the latency tool of Xenomai
Real-Time Performance Tunings
Sequentially tune virtualization through configurations of
BIOS, kernel, host, guest and QEMU
Comparison
Measure the latency difference with the latency tool
Validation
Measure the latency difference with a real-time robotic application

## Slide 5: Application Context and Conditions
This work was written at SIGMATEK GmbH & Co KG
Host OS: Ubuntu 22.04.4 LTS, PREEMPT-RT
Guest OS: Salamander 4
  Built with Yocto [1]
  Virtualized through Quick Emulator (QEMU) [2]
  Hard real-time with Xenomai 3 [3]
Trace-cmd [4] and Kernelshark [5] for kernel tracing and visualization

## Slide 6: Results – Latency Tool
10 minutes with a sampling period of 100 µs, priority of 99
Table 1: Comparison of Latency Statistics
Figure 1: Comparison of Latency Distributions
Samples
Time in μs

## Slide 7: Results – Robotic Application
Difference between command issuance time and signal arrival at PWM
1,000 samples
Table 2: Comparison of Robotic Application Latency Statistics

## Slide 8: Discussion
Latency Tool
Worst latency decreased from 707.622 µs to 17.134 µs
No overruns
Close to bare metal’s 10.709 µs
Goal achieved
Robotic Application
Worst latency dropped from 129 ms to 3.988 ms
Close to bare metal’s 1.49 ms
Tunings validated

## Slide 9: Outlook
Additional configurations
Other hypervisors and virtualization technologies
More testing under workloads

## Slide 10: References
[1] https://ubuntu.com/blog/what-is-real-time-linux-ii
[2] https://docs.yoctoproject.org/
[3] https://www.qemu.org/
[4] https://xenomai.org/
[5] https://trace-cmd.org/
[6] https://kernelshark.org/

## Slide 11: QEMU Script

## Slide 12: Xenomai Approaches

## Slide 13: Salamander 4 Virtualization QEMU Configurations

## Slide 14: Robot

## Slide 15: Servo Motor with PWM module

## Slide 16: Servo Motor Function

## Slide 17: Robotic Application Setups

## Slide 18: Robotic Application Flowchart

## Slide 19: Results of Robotic Application